#### FSTDC-3H-470 Series
TDC-3H-470 Series

#### Features

  Standardized mechanical dimensions and pinning

  Supply Voltage 5V or 9V or 12V

  VHF/UHF combinations with Hyper Band

  75 Ohm asymmetrical or symmetrical IF output optional

  RCA/IEC/f antenna terminal versions optional

  Voltage synthesized tuning or PLL synthesized tuning

#### Applications

  World wide TV reception

#### Standard Specifications(Typical models)

| TYPE | FSTDC-3H-470 FSTDC-3H1-470 FSTDC-3H2-470 | TDC-3H-470 TDC-3H1-470 TDC-3H2-470 | FSTDC-3HB-470 FSTDC-3H1B-470 FSTDC-3H2B-470 | TDC-3HB-470 TDC-3HB1-470 TDC-3HB2-470 |
| --- | --- | --- | --- | --- |
| SYSTEM | PAL D/K | PAL D/K | PAL B/G | PAL B/G |
| TUNING | PLL | VS | PLL | VS |
| BAND(MHZ) | L H U | 49.75-168.25 176.25-464.25 471.25-863.25 | 49.75-168.25 176.25-464.25 471.25-863.25 | 48.25-168.25 175.25-463.25 471.25-855.25 | 48.25-168.25 175.25-463.25 471.25-855.25 |
| 1.F(MHZ) | fip fip fip | 38.0 31.5 33.57 | 38.0 31.5 34.47 | 38.9 33.4 34.47 | 38.9 33.4 34.47 |
| SUPPLY VOLTAGE(v) | 5 or 9 or 12 | 5 or 9 or 12 | 5 or 9 or 12 | 5 or 9 or 12 |
| POWER GAIN(DB) | 32min | 32min | 32min | 32min |
| NOISE FIGURE(DB) | 9max | 9max | 9max | 9max |
| V.S.W.R | 5max | 5max | 5max | 5max |
| I.F.REJ. (DB) | VHF:51min UHF:70min | VHF:51min UHF:70min | VHF:50min UHF:70min | VHF:50min UHF:70min |
| IMAGE REJ. (DB) | VHF:51min UHF:46min | VHF:51min UHF:46min | VHF:51min UHF:46min | VHF:51min UHF:46min |
| 1%CORSS MODULATION | 85dB V type | 85dB V type | 85dB V type | 85dB V type |
| PLL | I square C | - | I square C | - |

#### Outline Dimensions

| TYPE | OUTLINE DIMENSIONS | TERMINAL |
| --- | --- | --- |
| FSTDC-3H-470 FSTDC-3HB-470 | A | FSS |
| FSTDC-3H1-470 FSTDC-3H1B-470 | B | FSS |
| FSTDC-3H2-470 FSTDC-3H2B-470 | C | FSS |
| TDC-3H-470 TDC-3HB-470 | A | VSS |
| TDC-3H1-470 TDC-3H1B-470 | B | VSS |
| TDC-3H2-470 TDC-3H2B-470 | C | VSS |

| OUTLINE DIMENSIONS | L | I | D | d |
| --- | --- | --- | --- | --- |
| A | 67.1 | 16.3 | 11.2 | 2.36 |
| B | 60.1 | 9.3 | 8.3 | 3.5 |
| C | 69.9 | 18.8 | 11.2 | 2.36 |

| TERMINALS | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FSS | AGC | BT | AS | SCL | SDA | NC | +B | NC | 30V | NC | IF |
| VSS | AGC | BT | BU | BH | BL | +B | NC | NC | NC | NC | IF |