#### TDC-3T-470 Series

#### feaTures

  - compact

  - High sensiTiviTy & low noise

  - VHF/UHF combinaTion(wiTh CATV ch.opTional)

  - PAL/NTSC versions available for various TV sysTems

#### ApplicaTions

  - Conventional color TV

#### Standard Specifica Tions (Typical Models)

| TYPE | TDC-3T-470 | TDC-3TB-470 |
| --- | --- | --- |
| SYSTEM | PAL D/K | PAL B/G |
| BAND(MHZ) | L H U | 49.75-160.25 168.25-464.25 471.25-863.25 | 48.25-161.25 168.25-463.25 471.25-855.25 |
| 1.F(MHZ) | fip fip fip | 38.0 31.5 33.57 | 38.9 33.4 34.47 |
| SUPPLY VOLTAGE(v) | 12 | 12 |
| I/O IMPEDANCE() | 75 | 75 |
| POWER GAIN (DB) | VHF:32min UHF:30min | VHF:32min UHF:30min |
| NOISE FIGURE (DB) | VHF:9max UHF:10max | VHF:8max UHF:10max |
| V.S.W.R | VHF:5max UHF:4max | VHF:5max UHF:4max |
| I.F.REJ. (DB) | VHF:50min UHF:70min | VHF:50min UHF:70min |
| IMAGE REJ. (DB) | VHF:50min UHF:46min | VHF:50min UHF:46min |
| 1%CORSS MODULATION | 74dB V min | 74dB V min |

#### OuTline Dimensions

| TYPE | L | I | D | d | A |
| --- | --- | --- | --- | --- | --- |
| TDC-3T-470 TDC-3TB-470 | 73.9 | 32 | 11.2 | 2.36 | 6.5 |
| TDC-3T5-470 TDC-3T5B-470 | 71.4 | 38.6 | 11.2 | 2.36 | 6.5 |
| TDC-3T7-470 TDC-3T7B-470 | 64.4 | 34.5 | 8.3 | 3.5 | 6.5 |
| TDC-3T8-470 TDC-3T8B-470 | 73.9 | 38.6 | 11.2 | 2.36 | 6.5 |
| TDC-3T10-470 TDC-3T10B-470 | 73.9 | 34.5 | 11.2 | 2.36 | 5.1 |
| TDC-3T15-470 TDC3T15B-470 | 73.9 | 34.5 | 11.2 | 2.36 | 6.5 |

| TERMINALS | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TERMINALS NAME | BU | BT | BH | AGC | BL | AFC | BM | IF | ANT |
| SUPPLY VOLTAGE(V) | +12 | 0-30 | +12 | +7.5 | +12 | +6.8 | +12 | - | - |