#### TDC-4A-470 Series
TDQ-4ASeries

#### Features

  Super compact

  Low cost design

  VHF&UHF combinations

  VHF&UHF combinations plus CATV (300MHz) ch available

#### Applications

  Portable colour or Black & with TV

  Radio receiver combined with TV band

#### Standard Specifications(Typical models)

| TYPE | TDC-4AB-300 | TDQ-4AB | TDC-4A-300 | TDQ-4A | TDQ-4AM |
| --- | --- | --- | --- | --- | --- |
| SYSTEM | Normal B/G plus CATV(300MHz) | Normal B/G | Mormal D/K plus CATV(300MHz) | Normal D/K | Normal M |
| BAND(MGZ) | L H U | 48.25-112.25 119.25-294.25 471.25-855.25 | 48.25-62.25 175.25-224.25 471.25-855.25 | 49.75-112.25 120.25-288.25 471.25-863.25 | 49.75-85.25 168.25-216.25 471.25-863.25 | 55.25-83.25 175.25-211.25 471.25-885.25 |
| 1.F(MGZ) | fip fip | 38.9 33.4 | 38.9 33.4 | 38.0 31.5 | 38.0 31.5 | 45.75 41.25 |
| SUPPLY VOLTAGE(v) | 9 | 9 | 9 | 9 | 9 |
| I/O ImPEDANCE(ЎЙ) | 75 | 75 | 75 | 75 | 75 |
| POWER GAIN(DB) | VHF:22min UHF:28min | VHF:28min UHF:28min | VHF:22min UHF:28min | VHF:28min UHF:28min | VHF:28min UHF:28min |
| NOISE FIGURE(DB) | VHF:12max UHF:14max | VHF:10max UHF:14max | VHF:12max UHF:14max | VHF:10max UHF:14max | VHF:10max UHF:14max |
| V.S.W.R | VHF:10max UHF:8max | VHF:10max UHF:8max | VHF:10max UHF:8max | VHF:10max UHF:8max | VHF:0.10max UHF:0.12max |
| I.F.REJ. (DB) | VL:30min VH:45min UHF:50min | VL:30min VH:45min UHF:50min | VL:30min VH:45min UHF:50min | VL:30min VH:45min UHF:50min | VL:30min VH:45min UHF:50min |
| IMAGE REJ. (DB) | VL:40min VH:30min UHF:18min | VL:40min VH:30min UHF:18min | VL:40min VH:30min UHF:18min | VL:40min VH:30min UHF:18min | VL:40min VH:30min UHF:18min |

#### Outline Dimensions

| TERMINALS | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TDC-4AB-300 TDC-4A-300 | ANT | AGC | BU | VT | BH | BL | NC | BM | IF | NC |
| TDQ-4AB TDQ-4A TDQ-4AM | ANT | AGC | BU | VT | BH | BL | NC | BM | IF | NC |